## Slide 1
Cisco Packet Tracer
— From Software Basics to Two Network Labs
EE6108 · LAB TEACHING
Notes: Welcome. This session uses two labs to teach the Packet Tracer workflow: build, configure, verify, and explain.

## Slide 2
What You Will Be Able to Do
Two labs, one workflow: build → configure → verify → explain
2
01
Build
Place PCs, switches, and routers, choose the right cable, and complete the physical topology.
02
Configure
Set PC addresses and gateways, enable router interfaces, and add static routes.
03
Verify
Use ping, tracert, and show commands to prove what works and explain what does not.
Two labs
LAB 01
Same subnet vs. cross-subnet
IP / mask / gateway
LAB 02
Static routing with 3 routers
ip route / routing table
Topology files: 1.pkt and 2.pkt
Goal: complete both labs independently and explain every result with evidence from the CLI.
Notes: Set expectations: this is a hands-on workflow, not a tour of every button.

## Slide 3
Contents
CONTENTS
3
01
Get Started
Interface layout and the role of Packet Tracer
02
Build and Configure
Devices, cables, Config/CLI, IP addressing
03
Two Labs
Same-subnet connectivity and three-router static routing
04
Troubleshoot and Summary
Symptoms, checklists, and the L2/L3 picture
Notes: Four sections: software basics, build/configure, the two labs, and troubleshooting.

## Slide 4
01
Get Started
Notes: Section one: understand the workspace before touching a device.

## Slide 5
What Is Packet Tracer?
A network simulation and teaching platform
5
Network simulation
Drag devices, cable them, and configure them to mimic real forwarding behavior.
No hardware required
Two labs, one platform
LAN addressing and connectivity, then multi-router static routing.
Same workflow
✓
Evidence, not animation
Use ping and show output as evidence; the CLI result is what counts.
CLI first
Packet Tracer is Cisco’s official network simulation tool. In this lesson it is used for one purpose: turning the lab manual topologies into configurable, testable networks.
Working rule: topology matches the manual, addresses match the table, and conclusions match the CLI output.
Notes: Emphasise evidence. Students should not say “it works” without a ping or show output.

## Slide 6
Interface Overview: Five Areas
Know where to choose devices, where to cable, and where to read status
6
Actual window: Lab 1 topology in 1.pkt.
1
Top: menu bar + main toolbar
File / Edit / Options / View / Tools; new, save, zoom, inspect, delete.
2
Center: workspace
Drop devices, draw cables, add text notes; the topology lives here.
3
Lower left: device palette
Choose PCs, switches, routers, and cables by category.
4
Lower right: Realtime / Simulation
Keep Realtime for these labs; the clock shows elapsed time.
5
Bottom: Scenario / Event List
Records events and PDUs; observation only in this lesson.
Notes: Use the actual Lab 1 window. Keep students in Realtime mode; they do not need Simulation for these two labs.

## Slide 7
02
Build and Configure
Notes: Section two: the shared procedure used by both labs.

## Slide 8
Step 1: Add Devices
Drag from the device palette into the workspace; core devices first
8
Category | Device / model | Role in these labs | Used in
End devices | PC-PT | Configure IP / mask / gateway; run ping tests | Lab 1, 2
Switches | 2960-24TT | Layer 2 forwarding inside the LAN | Lab 1, 2
Routers | Router-PT (2911) | Layer 3 forwarding and static routes | Lab 2
Cables | Automatically Choose | Automatically selects the correct cable type | Lab 1, 2
Cables | Copper Straight-Through | PC ↔ switch when a manual choice is required | Lab 1, 2
Place switches and routers first, then the PCs; leave room for network labels.
Notes: Only five device types are needed. The “Used in” column prevents students from adding equipment the labs do not require.

## Slide 9
Step 2: Choose the Right Cable
A wrong cable is one of the most common reasons a link stays down
9
Auto-connect (recommended)
· Orange lightning icon
· Chooses by port type
· Used in both labs
· No pinout decision
Straight-through
· PC ↔ switch
· Same pinout both ends
· Most common LAN cable
· Different device classes
Crossover
· Switch ↔ switch
· Router ↔ router
· 2960 supports Auto-MDIX
· Same device classes
Course convention
Both labs use Automatically Choose Connection Type. Only override it when the task explicitly asks for a cable type.
Notes: In practice students should use auto-connect. If a link is down, check cable and interface before changing IP settings.

## Slide 10
Two Ways In: Config and CLI
The GUI is easier for PCs; the CLI is closer to real equipment
10
Config tab
For PCs
Double-click the PC → Config
Set IP, mask, default gateway
Graphical and immediate
Limited for advanced router features
Use for: all PC addresses
CLI
For network devices
Double-click the device → CLI
Interfaces, static routes, verification
Matches Cisco IOS
Start with enable, then configure terminal
Use for: routers and switches
Course convention: PC settings in Config; router and switch settings in CLI.
Notes: Keep the split clean. PC addressing is faster in Config; everything routed or switched is configured in CLI.

## Slide 11
IOS Command Modes
The prompt tells you which commands are available
11
>
User EXEC
Router>
View basic information; no configuration changes.
Enter: enable
#
Privileged EXEC
Router#
show, save, debug; enter global configuration.
Enter: configure terminal
cfg
Global config
Router(config)#
Hostname, static routes, and global settings.
Enter: interface g0/0
if
Interface config
Router(config-if)#
IP address, no shutdown, interface settings.
Enter: exit / end
Router> enable → Router# configure terminal → Router(config)# interface g0/0 → Router(config-if)# ip address …
If the prompt is wrong, the command will be wrong.
Notes: Use the prompt to orient students. They should know how to move between modes before the router lab.

## Slide 12
Configure a PC: Config → FastEthernet0
Address, mask, and gateway decide where the packet goes
12
PC0
IP Configuration
Physical
Config
Desktop
Programming
Attributes
Static
DHCP
IPv4 Address
192.168.1.1
Subnet Mask
255.255.255.0
Default Gateway
192.168.1.254
DNS Server
(optional; not used here)
Press Enter or click away; verify with ipconfig.
Same subnet
The gateway may be left blank. In Lab 1, both PCs use the same /24.
Different subnet
The default gateway is required. In Lab 2, the PC hands remote packets to the router.
Check yourself first
One wrong address, mask, or gateway breaks ping; run ipconfig before blaming the network.
Mask answers “is the destination local?” The gateway answers “how does it leave?”
Notes: Connect this to Lab 1: the first failure is caused by a wrong mask/network, with no gateway available.

## Slide 13
Router Interfaces: Assign, Enable, Verify
Router interfaces are administratively down until no shutdown is entered
13
Actual CLI from 2.pkt — Router0 after interface and static-route configuration.
Default state: down
A router interface starts in shutdown; enter no shutdown under the interface.
Address must match
The interface IP and mask must belong to the connected subnet; LAN gateways use .254 here.
Verify up/up
Use show ip interface brief and show ip route to confirm both state and reachability.
A red link is not always a wrong IP: check no shutdown first, then the address and mask.
Notes: This is the actual Router0 CLI from 2.pkt. Point to enable, show ip route, and the static route marked S.

## Slide 14
Before Lab 1: Build an Evidence Chain with ping
Use the same order every time; do not start by pinging the far end
14
01
Same subnet: ping the peer
Proves the link, mask, and Layer 2 forwarding are correct.
02
Different subnet: ping the gateway first
If the gateway replies but the far end does not, look at routing.
03
Still failing: run tracert
The first timed-out hop shows where forwarding stops.
04
Record the result
Reply / timeout / unreachable, plus loss, becomes your evidence.
Actual CLI from 1.pkt: four timeouts, 100% loss.
Read the output
The command is correct; the address plan is not. Four sent, zero received: PC0 has no way to reach 192.168.2.1.
Reply from …
Link and configuration are basically correct
Request timed out
No reply: routing, gateway, or physical link
Host unreachable
Cannot deliver locally: gateway / ARP / subnet
Notes: This slide establishes the verification language used in both labs: reply, timeout, unreachable, and loss.

## Slide 15
03
Two Labs
Notes: Section three: the two experiments. Each starts from its actual topology and uses CLI screenshots as evidence.

## Slide 16
Two Labs: From Local Switching to Static Routing
Each lab adds one capability; Lab 1 is the foundation for Lab 2
16
Lab | Topology | Core skill | Success criterion
01 LAN addressing | 1 switch + 2 PCs | IP / mask, same-subnet test | After correcting PC1, ping succeeds
02 Static routing | 3 routers + 2 switches + 2 PCs | Default gateway, ip route | PC0 reaches PC1 with 0% loss
One method
Shared workflow: build → assign addresses → configure forwarding → ping → explain the result. The commands change; the method does not.
Notes: Frame the two labs as a sequence. Lab 1 teaches local delivery; Lab 2 adds a gateway and routing.

## Slide 17
Lab 1: Same Subnet vs. Cross-Subnet
LAB 01 · one 2960 switch + two PCs; create a failure, then correct it
17
Original topology: 1.pkt (PC0 / PC1 / 2960-24TT)
Lab goal
· Cable PC–switch–PC · Ping across subnets and fail · Correct PC1 and succeed
Device | Initial IP | Corrected
PC0 | 192.168.1.1 | 192.168.1.1
PC1 | 192.168.2.1 | 192.168.1.2
Switch0 | — | Layer 2
Mask 255.255.255.0; gateway left blank.
Task: PC0 pings 192.168.2.1 (fail) → change PC1 to 192.168.1.2 → ping again (success).
Notes: Start with the actual 1.pkt topology. The failure is intentional: it makes the subnet mask visible.

## Slide 18
Lab 1 Procedure: Fail, Correct, Verify
The screenshots below are the real CLI output from 1.pkt
18
1
Place and cable
2 × PC-PT and 1 × 2960-24TT; PC0 to Fa0/1, PC1 to Fa0/2.
2
Set the initial addresses
PC0 192.168.1.1/24; PC1 192.168.2.1/24; leave the gateway blank.
3
Test the failure
From PC0, ping 192.168.2.1; expect four timeouts.
4
Correct PC1 and retest
Set PC1 to 192.168.1.2/24; ping 192.168.1.2; expect 0% loss.
PC0 → 192.168.2.1: 100% loss
PC0 → 192.168.1.2: 0% loss, TTL=128
Compare the two
The only change between the two screenshots is PC1’s IP address.
Notes: These are real captures from 1.pkt. Ask students to compare loss, reply lines, and TTL.

## Slide 19
Lab 1: Why Did the First Ping Fail?
The switch was fine; the two hosts had different network IDs
19
PC0
192.168.1.1/24
Network 192.168.1.0
≠
PC1
192.168.2.1/24
Network 192.168.2.0
≠
No gateway → packet cannot leave
PC0 treats PC1 as remote. With no default gateway, it cannot hand the packet to a router, so it is dropped locally.
1
Network ID
IP AND mask. With /24, the first three octets must match.
2
Switch role
A Layer 2 switch reads the destination MAC and forwards the frame; it does not change IP addresses.
3
Correction
Change PC1 to 192.168.1.2. Both hosts now share 192.168.1.0/24.
Q1 Does the switch change the IP?
No. It looks only at the destination MAC and its MAC address table.
Q2 What does the mask do?
It separates network bits from host bits and decides local vs. remote.
Conclusion: same subnet is not “same switch”; it means the same network ID.
Notes: The first ping failed because PC1 was remote and PC0 had no gateway. The switch itself was doing its L2 job.

## Slide 20
Lab 2: Three Routers and Static Routing
LAB 02 · 2 PCs + 2 switches + 3 routers; four /24 networks
20
Original topology: 2.pkt (PC0–Route0–Route1–Route2–PC1)
Lab goal
· PC gateways configured · All router links up/up · Bidirectional static routes
Area | Network | Gateway / link
Orange LAN | 192.168.1.0/24 | R0 G0/0/0 .254
Blue transit | 192.168.10.0/24 | R0 .1 ↔ R1 .2
Red transit | 192.168.20.0/24 | R1 .3 ↔ R2 .4
Yellow LAN | 192.168.2.0/24 | R2 G0/0/1 .254
PC0 .1 and PC1 .1; all masks /24.
Task: configure host gateways, router interfaces, and both forward and return static routes.
Notes: This is the actual 2.pkt topology. Point out the four subnets and the three-router chain.

## Slide 21
Lab 2: Interfaces and Static Routes
Use CLI output from 2.pkt to confirm what each router knows
21
Route0: S 192.168.2.0/24 via 192.168.10.2
Route1: S 192.168.1.0 via .10.1 and 192.168.2.0 via .20.4
Router | Destination | Mask | Next hop
Route0 | 192.168.2.0 | 255.255.255.0 | 192.168.10.2
Route1 | 192.168.2.0 | 255.255.255.0 | 192.168.20.4
Route1 | 192.168.1.0 | 255.255.255.0 | 192.168.10.1
Route2 | 192.168.1.0 | 255.255.255.0 | 192.168.20.3
Static-route pattern: ip route <destination> <mask> <next hop>. Every router needs a forward and a return path.
Notes: These are real screenshots of show ip route. The table summarises all four routes that must exist.

## Slide 22
Lab 2: End-to-End Verification and Failure Cases
A successful ping is the result; explaining where it can fail is the goal
22
PC0 → PC1: 0% loss, TTL 125 (three routers)
No return route on Route2
The request reaches PC1, but the reply has no route back to 192.168.1.0 and is dropped. PC0 times out.
Missing route on Route1
The packet reaches Route1, which has no route to 192.168.2.0; forwarding stops and PC0 times out.
No default gateway on PC0
PC0 treats the remote destination as local and cannot deliver the frame; the ping fails immediately.
Read the evidence
TTL 125 = 128 − 3. The packet crossed three routers, matching the path in the topology.
Fixed order
Troubleshooting order: PC gateway → interface up/up → show ip route → return route → ping again.
Notes: Use the actual ping capture. TTL 125 is strong evidence that the packet crossed three routers.

## Slide 23
04
Troubleshoot and Summary
Notes: Section four: turn the two labs into a reusable troubleshooting method.

## Slide 24
Troubleshooting: Match the Symptom to the Layer
Check physical → Layer 2 → Layer 3, and change one variable at a time
24
Symptom | Most likely cause | Check first | Action
Link LED off or red | Wrong cable or interface shutdown | Both ends; interface state | Replace cable; no shutdown
Same-switch PC cannot ping | IP / mask not in the same subnet | ipconfig on both PCs | Use the same network ID
Gateway replies, far end does not | Missing route or return route | show ip route on each router | Add forward and return routes
First ping times out, later replies | ARP resolution or convergence | Second ping; ARP entry | Wait and retest; not a config fault
Router link stays down | Interface still administratively down | show ip interface brief | Enter no shutdown
Discipline
Do not change three things at once. If you do, a working network will not tell you which change fixed it.
Notes: Only the symptoms that occur in Labs 1 and 2 are included. The first-ping timeout is real and was observed in 2.pkt.

## Slide 25
Submission Checklist
Check each item as you finish a lab, not after writing the report
25
Shared
Topology matches the manual; labels are clear
All PC addresses, masks, and gateways checked
Key interfaces are up/up
Every test has a CLI capture or written record
Lab 1
Initial failure captured (100% loss)
PC1 corrected to 192.168.1.2/24
Second ping shows 0% loss
Can explain why the first ping failed
Lab 2
Both PC gateways configured
Three routers have interface addresses
Four static routes installed
PC0 reaches PC1 with 0% loss
Report
Configuration commands included
Verification output included
Result explained in your own words
Screenshots match the stated conclusion
Report standard
A report needs three kinds of evidence: the command, the output, and the explanation that connects them.
Notes: Use this as a formative checklist. Students should tick items immediately after each lab.

## Slide 26
How the Two Labs Connect
Same forwarding question, two different layers
26
LAB 01
Same subnet
Host resolves the peer MAC; switch forwards the frame.
L2 local delivery
LAB 02
Different subnet
Host sends to the gateway; routers forward hop by hop.
L3 routed delivery
Same subnet → MAC
The destination is local; ARP gives the destination MAC and the switch forwards.
Different subnet → IP route
The destination is remote; the host uses the gateway and each router looks up the destination network.
Address before conclusion
A ping result only makes sense after you know the address, gateway, interface state, and route table.
One question: is the destination local? If yes, L2; if no, gateway and L3.
Notes: This is the conceptual bridge: Lab 1 is local L2 delivery; Lab 2 is gateway plus L3 routing.

## Slide 27
Three Things to Take Away
Methods matter more than memorising a single command
27
01
Physical before logical.
If the link is down, check cable, interface state, and no shutdown before changing IP settings.
02
Direct before remote.
Ping the peer on the same subnet; for a remote target, ping the gateway first, then the far end.
03
Evidence before conclusion.
A screenshot is not proof by itself; connect the command, the output, and the reason.
After class
Next: complete 1.pkt and 2.pkt, then submit command → output → explanation for each required test.
Notes: Close with three habits: physical first, direct first, evidence first.

## Slide 28
Thank You
Questions & Discussion
EE6108 · Cisco Packet Tracer · Labs 1 and 2
Lab Teaching
Notes: End of session. Remind students to use the checklist before submitting.